## Slide 1: Chemistry of Environment
Green Technology

## Slide 2: GREEN CHEMISTRY
DEFINITION
  Green Chemistry is the utilisation of a set of principles that reduces or eliminates the use or generation of hazardous substances in the design, manufacture and application of chemical products .

## Slide 3: Green Chemistry Is About...
Cost
Waste
Materials
Hazard
Risk
Energy
Reducing

## Slide 4: The 12 Principles of Green Chemistry (1-6)

## Slide 5: The 12 Principles of Green Chemistry (7-12)
    7 Use of Renewable Feedstocks
      A raw material or feedstock should be renewable rather than depleting whenever technically and economically practicable.
eg. Vegetable oil+methanol=biodiesel+glycerine
    8 Reduce Derivatives
      Unnecessary derivatization (use of blocking groups, protection/de-protection, and temporary modification of physical/chemical processes) should be minimised or avoided if possible, because such steps require additional reagents and can generate waste.
    9 Catalysis
      Catalytic reagents (as selective as possible) are superior to stoichiometric reagents.
    10 Design for Degradation
      Chemical products should be designed so that at the end of their function they break down into innocuous degradation products and do not persist in the environment.
    11 Real-time Analysis for Pollution Prevention
      Analytical methodologies need to be further developed to allow for real-time, in-process monitoring and control prior to the formation of hazardous substances.
    12 Inherently Safer Chemistry for Accident Prevention
      Substances and the form of a substance used in a chemical process should be chosen to minimise the potential for chemical accidents, including releases, explosions, and fires.

## Slide 6: 1. Prevention
It is better to prevent waste than to treat or clean up waste after it is formed.

## Slide 7: “It is better to prevent waste than to treat or clean up waste after it is formed”
Chemical
Process

## Slide 8: GREEN DESIGNS Products that avoid using toxic materials Will not harm the humans or ecological system
Reusable diaper cover (the gPants)
Disposable (inserts)
100% biodegradable.
Environmentally friendly
Cheaper to manufacturer
Life span-30+ yrs.
Electrically efficient
Biodegradable recyclable and/or reusable parts
Made eco-friendly materials
eDiapers
LED Frog Lightbulbs
Green Computers

## Slide 9
“Green technology” is in the early stage of development;
however it is becoming the new wave of society.
It encompasses an evolving group of methods and techniques;
Manufacturing of Green Designs
Incorporating Renewable Energy or Alternatives
“Greening” Technology
Such as
The Goal:
To be Sustainable for everyone everyday
The Expectation:
To change the daily habitual habits of society.
Notes: We must be able to sustain our renewable energy and alternative resources in a way that will not harm the planet.

## Slide 10
eDiapers Comes in different
colors & sizes
Can be flushed-composted
Features lower power consumption
Designed for disassembly so that it can easily be broken down and recycled
LED Frog lightbulbs
Ties in with traditional lightbulb
requires no harmful chemical to produce
The invention, design, and execution of such products are vital to GREEN TECHNOLOGY
Reducing waste by changing patterns of production

## Slide 11: Environmental Disasters
Love Canal
  in Niagara Falls, NY a chemical and plastics company had used an old canal bed as a chemical dump from 1930s to 1950s. The land was then used for a new school and housing track. The chemicals leaked through a clay cap that sealed the dump. It was contaminated with at least 82 chemicals (benzene, chlorinated hydrocarbons, dioxin). Health effects of the people living there included: high birth defect incidence and siezure-inducing nervous disease among the children.
http://ublib.buffalo.edu/libraries/projects/lovecanal/

## Slide 12: 2. Atom Economy
Synthetic methods should be designed to maximize the incorporation of all materials used in the process into the final product.

## Slide 13: Percent yield:
Percent yield:
  % yield = (actual yield/theoretical yield) x 100
What is missing?
What co-products are made?
How much waste is generated?
Is the waste benign waste?
Are the co-products benign and/or useable? How much energy is required?
Are purification steps needed?
What solvents are used? (are they benign and/or reusable?
Is the “catalyst” truly a catalyst? (stoichiometric vs. catalytic?)

## Slide 14: Balanced Reactions
Balanced chemical reaction of the epoxidation of styrene

## Slide 15: Atom Economy:
Atom Economy
% AE = (MW of Desired Product/MW of all reactants) X 100
Balanced Equations
Focuses on the reagents
Stoichiometry?
How efficient is the reaction in practice?
Solvents?
Energy?

## Slide 16: Atom Economy
Balanced chemical reaction of the epoxidation of styrene
Assume 100% yield.
100% of the desired epoxide product is recovered.
100% formation of the co-product: m-chlorobenzoic acid
A.E. of this reaction is 23%.
77% of the products are waste.

## Slide 17: 3. Less Hazardous Chemical Synthesis
Whenever practicable, synthetic methodologies should be designed to use and generate substances that possess little or no toxicity to human health and the environment.

## Slide 18
Less Hazardous Chemical Synthesis
Disadvantages
  phosgene is highly toxic, corrosive
  requires large amount of CH2Cl2
  polycarbonate contaminated with Cl impurities
Polycarbonate Synthesis: Phosgene Process

## Slide 19
Less Hazardous Chemical Synthesis
Advantages
  diphenylcarbonate synthesized without phosgene
  eliminates use of CH2Cl2
  higher-quality polycarbonates
Polycarbonate Synthesis: Solid-State Process

## Slide 20
Alternative Synthetic Pathways Award Flexsys America L.P. New Process for 4-Aminodiphenylamine
Academic Award Terrence J. Collins Carnegie Mellon University TAML™ Oxidant Activators: General Activation of Hydrogen Peroxide for Green Oxidation Technologies
Eliminate use of acids to break initial bonds
Phosgene replacement

## Slide 21: 4. Designing Safer Chemicals
Chemical products should be designed to preserve efficacy of the function while reducing toxicity.

## Slide 22: Designing Safer Chemicals Case Study: Antifoulants (Marine Pesticides)

## Slide 23: Designing Safer Chemicals: Case Study: Antifoulants
Antifoulants are generally dispersed in the paint as it is applied to the hull. Organotin compounds have traditionally been used, particularly tributyltin oxide (TBTO). TBTO works by gradually leaching from the hull killing the fouling organisms in the surrounding area
TBTO and other organotin antifoulants have long half-lives in the environment (half-life of TBTO in seawater is > 6 months). They also bioconcentrate in marine organisms (the concentration of TBTO in marine organisms to be 104 times greater than in the surrounding water).
Organotin compounds are chronically toxic to marine life and can enter food chain. They are bioaccumulative.

## Slide 24: Designing Safer Chemicals: Case Study: Antifoulants
Presidential Green Chemistry Challenge Award, 1996
The active ingredient in Sea-Nine® 211, 4,5-dichloro-2-n-octyl-4-isothiazolin-3-one (DCOI), is a member of the isothiazolone family of antifoulants.

## Slide 25: 5. Safer Solvents and Auxiliaries
The use of auxiliary substances (solvents, separation agents, etc.) should be made unnecessary whenever possible and, when used, innocuous.

## Slide 26
Preferred | Useable | Undesirable
Water | Cyclohexane | Pentane
Acetone | Heptane | Hexane(s)
Ethanol | Toluene | Di-isopropyl ether
2-Propanol | Methylcyclohexane | Diethyl ether
1-Propanol | Methyl t-butyl ether | Dichloromethane
Ethyl acetate | Isooctane | Dichloroethane
Isopropyl acetate | Acetonitrile | Chloroform
Methanol | 2-MethylTHF | Dimethyl formamide
Methyl ethyl ketone | Tetrahydrofuran | N-Methylpyrrolidinone
1-Butanol | Xylenes | Pyridine
t-Butanol | Dimethyl sulfoxide | Dimethyl acetate
 | Acetic acid | Dioxane
 | Ethylene glycol | Dimethoxyethane
 |  | Benzene
 |  | Carbon tetrachloride
“Green chemistry tools to influence a medicinal chemistry and research chemistry based organization”
Dunn and Perry, et. al., Green Chem., 2008, 10, 31-36
Solvent Selection

## Slide 27
Undesirable Solvent | Alternative
Pentane | Heptane
Hexane(s) | Heptane
Di-isopropyl ether or diethyl ether | 2-MeTHF or tert-butyl methyl ether
Dioxane or dimethoxyethane | 2-MeTHF or tert-butyl methyl ether
Chloroform, dichloroethane or carbon tetrachloride | Dichloromethane
Dimethyl formamide, dimethyl acetamide or N-methylpyrrolidinone | Acetonitrile
Pyridine | Et3N (if pyridine is used as a base)
Dichloromethane (extractions) | EtOAc, MTBE, toluene, 2-MeTHF
Dichloromethane (chromatography) | EtOAc/heptane
Benzene | Toluene
Solvent replacement table
“Green chemistry tools to influence a medicinal chemistry and research chemistry based organization”
Dunn and Perry, et. al., Green Chem., 2008, 10, 31-36

## Slide 28: 6. Design for Energy Efficiency
Energy requirements should be recognized for their environmental and economic impacts and should be minimized. Synthetic methods should be conducted at ambient temperature and pressure.

## Slide 29: Energy in a chemical process
Thermal (electric)
Cooling (water condensers, water circulators)
Distillation
Photo
Microwave
Source of energy:
Power plant – coal, oil, natural gas

## Slide 30: Energy usage
Chemicals and petroleum industries account for 50% of industrial energy usage.
~1/4 of the energy used is consumed in distillation and drying processes.

## Slide 31: Alternative energy sources: Photochemical Reactions
Two commercial photochemical processes (Caprolactam process & vitamin D3)
Caprolactam process
NOCl  NO˙ + Cl˙ (535nm)
Notes: Vitamin D3: Photochemical electrocyclic ring opening followed by a thermal 1,7-hydride shift
no viable thermal alternative

## Slide 32: Alternative Energy Sources: Microwave chemistry
Wavelengths between 1 mm and 1 m
  Frequency fixed at 2.45 GHz
More directed source of energy
Heating rate of 10°C per second is achievable
Possibility of overheating (explosions)
Solvent-free conditions are possible
Interaction with matter characterized by penetration depth

## Slide 33: 7. Use of Renewable Feedstocks
A raw material or feedstock should be renewable rather than depleting whenever technically and economically practical.

## Slide 34
Petroleum Products [Hydrocarbons]
Biomaterials [Carbohydrates, Proteins, Lipids]
Highly Functionalized Molecules
Singly Functionalized Compounds [Olefins, Alkylchlorides]
Highly Functionalized Molecules

## Slide 35: Polymers from Renewable Resources: Poly(lactic acid)

## Slide 36: Raw Materials from Renewable Resources: The BioFine Process
Paper mill
sludge
Levulinic acid
Municipal solid waste
and waste paper
Agricultural
residues,
Waste wood
Green Chemistry Challenge Award 1999 Small Business Award

## Slide 37: Levulinic acid as a platform chemical
DALA (-amino levulinic acid)
(non-toxic, biodegradable herbicide)
Diphenolic acid
Acrylic acid
Succinic acid
THF
MTHF
(fuel additive)
butanediol
gamma
butyrolactone

## Slide 38: 8. Reduce Derivatives
Unnecessary derivatization (blocking group, protection/deprotection, temporary modification of physical/chemical processes) should be avoided whenever possible.

## Slide 39: Protecting Groups
2 synthetic steps are added each time one is used
Overall yield and atom economy will decrease
“Protecting groups are used because there is no direct way to solve the problem without them.”

## Slide 40
Eg= synthesis of m-hydroxy benzoic acid from m-hydroxy benzaldehyde

## Slide 41: 9. Catalysis
Catalytic reagents (as selective as possible) are superior to stoichiometric reagents.Use catalyst,not stiochiometric reagents.
Eg= propene+hydrogen=propane(100%)
Ni as catalyst

## Slide 42: Heterogeneous vs Homogenous
Distinct solid phase
Readily separated
Readily regenerated & recycled
Rates not as fast
Diffusion limited
Sensitive to poisons
Lower selectivity
Long service life
High energy process
Poor mechanistic understanding
Same phase as rxn medium
Difficult to separate
Expensive and/or difficult to separate
Very high rates
Not diffusion controlled
Robust to poisons
High selectivity
Short service life
Mild conditions
Mechanisms well understood

## Slide 43: Heterogeneous vs Homogenous
Distinct solid phase
Readily separated
Readily regenerated & recycled
Rates not as fast
Diffusion limited
Sensitive to poisons
Lower selectivity
Long service life
High energy process
Poor mechanistic understanding
Same phase as rxn medium
Difficult to separate
Expensive and/or difficult to separate
Very high rates
Not diffusion controlled
Robust to poisons
High selectivity
Short service life
Mild conditions
Mechanisms well understood
Green
catalyst

## Slide 44: Biocatalysis
Enzymes or whole-cell microorganisms
Benefits
  Fast rxns due to correct orientations
  Orientation of site gives high stereospecificity
  Water soluble
  Naturally occurring
  Moderate conditions

## Slide 45: 10. Design for Degradation
Chemical products should be designed so that at the end of their function they do not persist in the environment and instead break down into innocuous degradation products.

## Slide 46: Persistence
Early examples:
Sulfonated detergents
  Alkylbenzene sulfonates – 1950’s & 60’s
  Foam in sewage plants, rivers and streams
  Persistence was due to long alkyl chain
  Introduction of alkene group into the chain increased degradation
Chlorofluorocarbons (CFCs)
  Do not break down, persist in atmosphere and contribute to destruction of ozone layer
DDT
  Bioaccumulate and cause thinning of egg shells

## Slide 47
Degradation of Polymers:
Polylactic Acid
Manufactured from renewable resources
  Corn or wheat; agricultural waste in future
Uses 20-50% fewer fossil fuels than conventional plastics
PLA products can be recycled or composted
Cargill Dow

## Slide 48: Polymers from Renewable Resources: Polyhydroxyalkanoates (PHAs)
Fermentation of glucose in the presence of bacteria and propanoic acid (product contains 5-20% polyhydroxyvalerate)
Similar to polypropene and polyethene
Biodegradable

## Slide 49: 11. Real-time Analysis for Pollution Prevention
Analytical methodologies need to be further developed to allow for real-time in-process monitoring and control prior to the formation of hazardous substances.

## Slide 50
Real time analysis for a chemist is the process of “checking the progress of chemical reactions as it happens.”
Knowing when your product is “done” can save a lot of waste, time and energy!

## Slide 51: 12. Inherently Safer Chemistry for Accident Prevention
Substance and the form of a substance used in a chemical process should be chosen so as to minimize the potential for chemical accidents, including releases, explosions, and fires.

## Slide 52
Phosgene!
Cyanide!

## Slide 53
12. Inherently Safer Chemistry for Accident Prevention
Tragedy in Bhopal, India - 1984
In arguably the worst industrial accident in history, 40 tons of methyl isocyanate (MIC) were accidentally released when a holding tank overheated at a Union Carbide pesticide plant, located in the heart of the city of Bhopal. 15,000 people died and hundreds of thousands more were injured.

## Slide 54
Chemists try to avoid things that explode, light on fire,
are air-sensitive, etc.
In the “real world” when these things happen, lives are lost.

## Slide 55: Zero Waste Technology
Zero waste means designing and managing products and processes to systematically avoid and eliminate the volume and toxicity of waste and materials, conserve and recover all resources, and not burn or bury them.

## Slide 56: Tools of green chemistry
Green starting materials
eg. Adipic acid from D-glucose
Green reagent
eg. Styrene from benzene
eg. Styrene from benzene Green reaction eg. Synthesis of ibuprofen

## Slide 59: “The use of auxiliary substances (e.g. solvents, separation agents, etc.) should be made unnecessary wherever possible, and innocuous when used”

## Slide 60: Poly lactic acid (PLA) for plastics production

## Slide 61: Polyhydroxyalkanoates (PHA’s)

## Slide 62: Pollution Prevention Hierarchy
Increasing Greenness
Prevention & Reduction
Recycling & Reuse
Treatment
Disposal

## Slide 63
A United Nations Environment Program
CDM
Clean Development Mechanism
Applying CLEANER PRODUCTION to MULTILATERAL ENVIRONMENTAL AGREEMENTS

## Slide 64
The Clean Development Mechanism (CDM) is a key tool in the Kyoto protocol, allowing countries (Annex I countries) with emission reduction targets to undertake and benefit from greenhouse gas emission reductions in other (non-Annex I) countries.

## Slide 65
About Kyoto Protocol: United Nations Framework Convention on Climate Change – UNFCCC
The Kyoto Protocol is an amendment to UNFCCC that sets out specific targets to reduce GHG emissions from UNFCCC Annex I countries (or more correctly, from Kyoto Protocol Annex B countries – these are almost identical, with the exception for the few Annex I countries that have ratified UNFCCC but not the Kyoto protocol). The Kyoto protocol also provides tools and procedures for countries to work together to achieve the emission reduction targets, instead of each country only trying to achieve the targets on their own in their own country. The three key tools are:
Clean Development Mechanism (CDM)
Joint Implementation (JI)
Emission Trading

## Slide 66
Annex I refers to UNFCCC and is a list of countries that are committed to support developing countries to address climate change. These are more or less identical with the developed countries and economies in transition (former soviet union bloc members).
Annex B refers to the Kyoto Protocol and is a list that states the emission target for each country in Annex I.
However, as not all Annex I countries have ratified the Kyoto Protocol (notably USA), these two lists are not exactly the same. However, to avoid confusion the two terms are often use interchangeably.

## Slide 67
Signed in 1997; in force since 16 February 2005.
Ratified by more than 130 countries
  > Major non participants: USA and Australia.
Commits Annex 1 countries to reducing greenhouse gas emissions.
  > GHG emissions may be reduced by ~ 5% below 1990 levels in 2008-2012;
  > Individual, quantified emission targets for each industrialized country;
  > 6 greenhouse gas covered: CO2, CH4, N2O, HFC, PFC, SF6.
3 flexibility mechanisms for financing emission reduction abroad.
  > Clean Development Mechanism (CDM)
  > Joint Implementation (JI)
  > International Emissions Trading (ET)
Kyoto Protocol:
Notes: Slide 3 – About Kyoto Protocol
As is explained in more detail in module 3: “Introduction to UNFCCC”, the Kyoto Protocol is an amendment to UNFCCC that sets out specific targets to reduce GHG emissions from UNFCCC Annex I countries (or more correctly, from Kyoto Protocol Annex B countries – these are almost identical, with the exception for the few Annex I countries that have ratified UNFCCC but not the Kyoto protocol). The Kyoto protocol also provides tools and procedures for countries to work together to achieve the emission reduction targets, instead of each country only trying to achieve the targets on their own in their own country. The three key tools are:
Clean Development Mechanism (CDM)
Joint Implementation (JI)
Emission Trading

## Slide 68: OVERVIEW
CDM: the basic idea
What is the Clean Development Mechanism (CDM) ?
  > A mechanism that allows Annex B Countries to undertake GHG emission reduction projects in non-annex B countries, and to use the achieved emission reductions to meet their own emission goal.
  > In CDM projects, the Annex B country fund the project and provides any necessary know-how and technology transfer to the non-annex B country where the project is implemented.
  > CDM works because emission reductions are many times more expensive to achieve in Annex B countries than in non-Annex B countries (the opportunities for emission reduction are bigger there).
Make difference between Annex I and Annex B countries!
Notes: Slide 4 – CDM: the basic idea
This slide explains the basic idea with CDM.
To avoid confusion, please explain that:
Annex I refers to UNFCCC and is a list of countries that are committed to support developing countries to address climate change. These are mor3e or less identical with the developed countries and economies in transition (former soviet union bloc members).
Annex B refers to the Kyoto Protocol and is a list that states the emission target for each country in Annex I.
However, as not all Annex I countries have ratified the Kyoto Protocol (notably USA), these two lists are not exactly the same. However, to avoid confusion the two terms are often use interchangeably.

## Slide 69
Examples of CDM projects
Notes: Slide 5 – Examples of CDM projects opportunities

## Slide 70: OVERVIEW
CDM organisation and objectives
Rules, modalities and procedures of CDM are defined in:
  > Kyoto Protocol;
  > Follow-up decisions of COP;
  > Decisions of CDM Executive Board.
CDM EB (Executive Board):
  > Responsible for further development of CDM rules, and supervising implementation;
  > Composed of 10 members + 10 alternates;
  > Reports to the COP (Conference of the Parties).
Twin objectives of CDM:
  > Help Annex 1 countries meet their objectives in a cost-effective way;
  > Contribute to sustainable development of the host country.
Notes: Slide 7 – CDM organization and objectives
The practical function of CDM is defined in detail in the Kyoto Protocol and in a number of follow-up decisions by COP as well as in supporting documents issued by different bodies in UNFCCC. The most important body is the Executive Board.
The basic requirement for any CDM project are:
Actual and real reductions of GHG emissions must be achieved.
The project must contribute to sustainable development in the country where the CDM project is implemented

## Slide 71
BASICS
Additionality and baselines
“A project is eligible for CDM if greenhouse gas emissions are reduced below those that would have occurred in the absence of the CDM project.”
Years
GHG emissions (tCO2eq)
Project implementation
Emissions baseline
Emissions after the project
1. Validation of project design, baseline and monitoring plan
2. Verification / Certification of emission reductions
ADDITIONAL EMISSION REDUCTIONS
Notes: Slide 8 – Additionality and baselines
Additionality: A CDM project is additional if anthropogenic emissions of greenhouse gases by sources are reduced below those that would have occurred in the absence of the CDM project.
Baseline: The baseline for a CDM project is the scenario that reasonably represents the anthropogenic emissions by sources of greenhouse gases that would occur in the absence of the proposed project. The method for calculating the baseline is a key challenge for many CDM projects, and ach new baseline methodology need to be approved by the Executive Board. In principle, each type of CDM project has to have its own baseline methodology. Once this methodology id developed and approved, other projects of the same type can use the same baseline methodology to calculate their baseline emissions.

## Slide 72
BASICS
Where is CDM applicable ?
Renewable energy > Wind power > Solar > Biomass power > Hydro power | Waste management > Capturing of landfill methane emissions to generate power > Utilisation of waste and waste water emissions for generation of energy
Energy efficiency measures > Boiler and steam efficiency > Pumps and pumping systems > Efficient cooling systems > Back pressure turbines > etc… | 
Cogeneration in industries having both steam and power requirements | 
Power sector > Induction of new technologies which are efficient (thermal) > Reduction in technical T&D losses | 
Fuel switching > From fossil fuel to green fuel like biomass… | 
Electrical energy saving 1 kWh = 0.8 ~ 0.9 kg CO2
Power generation (waste heat / renewable) 1 MW = 4.000 ~ 5.000 t CO2
Coal saving 1 kg = 1.3 ~ 1.6 kg CO2
Fuel oil saving 1 litre oil = 3 ~ 3.5 kg CO2
NG based power generation 1 kWh generation = 0.35 ~ 0.45 kg CO2 1 kg NG burning/saving = 2.4 ~ 2.5 kg CO2
Notes: Slide 11 – Where is CDM applicable ?
Examples of eligible projects:
  - Fuel switch to lower carbon intensive fuels
  - Installations based on renewable energy
  - Combined heat and power (CHP)
  - Supply-side energy efficiency improvements
  - End-use energy efficiency improvements
  - Agriculture sector (except land-use change)
  - Reduction in methane emissions
  - Reforestation/afforestation projects
The box in this slide indicates how different savings may be translated to GHG emissions. Please note that this is only indicative!

## Slide 73
Environmental Impact Assessment
Environmental Impact Assessment (EIA) is a process of evaluating the likely environmental impacts of a proposed project or development, taking into account inter-related socio-economic, cultural and human-health impacts, both beneficial and adverse.

## Slide 74: Environment Impact Assessment (EIA) :Definition
In EIA, the term “impacts” is used instead of “effects of activities.”
What is an impact?
Environmental Impact Assessment is
A formal process for identifying:
  likely effects of activities or projects on the ENVIRONMENT, and on human health and welfare.
  means and measures to mitigate & monitor these impacts

Environment is broadly interpreted: physical, biological, and social.
Notes: Aspects of the environment:
Physical: soil & water resources, air quality
Biological: fauna, flora, ecosystem
Social: human health and welfare, culture, religion, and local values
Or: Economical, social and eco-systemic

## Slide 75: What is an impact?
The impact of an activity is a deviation (a change) from the baseline situation that is caused by the activity.
To measure an impact, you must know what the baseline situation is.
!
The baseline situation is the existing environmental situation or condition in the absence of the activity.
The baseline situation is a key concept in EIA.
More…

## Slide 76: The baseline situation
In characterizing the baseline situation, many environmental components MAY be of interest
Water Quantity, quality, reliability, accessibility
Soils Erosion, crop productivity, fallow periods, salinity, nutrient concentrations
Flora Composition and density of natural vegetation, productivity, key species
Fauna Populations, habitat
Special Key species ecosystems
Env Health Disease vectors, pathogens
The components of interest are those that are likely to be affected by your activity—or upon which your activity depends for its success
Notes: For example, an ecotourism activity might depend on water level in watering holes---but this environmental component is not in fact affected by your activity.

## Slide 77
EIA would necessarily involve the following stages:
1.Screening to determine which projects or developments require a full or partial impact assessment study;
2.Scoping to identify which potential impacts are relevant to assess (based on legislative requirements, international conventions, expert knowledge and public involvement), to identify alternative solutions that avoid, mitigate or compensate adverse impacts on biodiversity (including the option of not proceeding with the development, finding alternative designs or sites which avoid the impacts, incorporating safeguards in the design of the project, or providing compensation for adverse impacts), and finally to derive terms of reference for the impact assessment;

## Slide 78
3. Assessment and evaluation of impacts and development of alternatives, to predict and identify the likely environmental impacts of a proposed project or development, including the detailed elaboration of alternatives;
4.Reporting the Environmental Impact Statement (EIS) or EIA report, including an environmental management plan (EMP), and a non-technical summary for the general audience.
5. Review of the Environmental Impact Statement (EIS), based on the terms of reference (scoping) and public (including authority) participation.

## Slide 79
6. Decision-making on whether to approve the project or not, and under what conditions; and
7. Monitoring, compliance, enforcement and environmental auditing. Monitor whether the predicted impacts and proposed mitigation measures occur as defined in the EMP. Verify the compliance of proponent with the EMP, to ensure that unpredicted impacts or failed mitigation measures are identified and addressed in a timely fashion.

## Slide 80
In summary,
The full EIA study is a far more significant effort than the preliminary assessment.

It is reserved for activities for which screening or the preliminary assessment shows that significant impacts are likely.
The Full EIA study
Notes: The purpose of a Full EIA study is not to find that impacts will not be significant. Its purpose is to allow an informed decision to be made about which significant environmental impacts may be acceptable to obtain a particular development objective. The preliminary assessment cannot serve this function.

## Slide 81: Conclusion
Green chemistry Not a solution to all environmental problems But the most fundamental approach to preventing pollution.

## Slide 82
Thank you