## Slide 1: MOSPF and PIM

## Slide 2: Taxonomy of common multicast protocols

## Slide 3
Multicast link state routing uses the source based tree approach

## Slide 4: MOSPF(1)
Group membership LSA is flooded throughout the AS
The router calculates the shortest path trees on demand (when it receives the first multicast packet)
MOSPF is a data-driven protocol; the first time an MOSPF router see a datagram with a given source and group address, the router constructs the Dijkstra shortest path tree

## Slide 5: MOSPF(2)
The shortest path tree is made all at once instead of gradually (i.e. pre-made, pre-pruned, ready to use)

## Slide 6: MOSPF with Areas (1)
Group management
  Group-membership LSA is flooded in the same area.
  Inter-area multicast forwarders (area border routers) summarize their attached areas' group membership to the backbone.
Data routing
  Introduction of the wild-card multicast receivers (area border routers)

## Slide 7: MOSPF with Areas(2)
Data routing (cont)
  In the presence of OSPF areas, during tree pruning care must be taken so that the branches leading to other areas remain, since it is unknown whether there are group members in these (remote) areas.
  For this reason, only those branches having no group members nor wild-card multicast receivers are pruned when producing the datagram shortest-path tree.

## Slide 8: MOSPF with Areas(3)
Data routing (cont)
  1. Source area: building intra-area shortest path tree (forward cost) with leaf nodes including wild-card multicast receivers.
  2. Backbone area: each wild-card multicast receiver of the source area calculates the shortest path from the source to the multicast forwarders (with group members) of other areas using the reverse cost.
  (You must know the reason why using the reverse cost in this case)

## Slide 9: MOSPF with Areas(4)
Data routing (cont)
  E.g. In Figure 4 of the sample MOSPF area configuration in the supplementary document, RT3 and RT4 can calculate and compare to determine which one of them should construct the shortest path from the source to RT7, RT10, and RT11 (the multicast forwarders in non-source areas). The result tree is shown in Figure 9 in the supplementary document.

## Slide 10: MOSPF with Areas(5)
Data routing (cont)
  3. Destination areas: The corresponding multicast forwarder (e.g. RT7 in area 2) constructs the shortest path using the reverse cost to each network (with group members) in its own area.

## Slide 12: MOSPF Tree in Source Area

## Slide 13: MOSPF Tree in Backbone Area

## Slide 14: MOSPF Tree in Destination Area

## Slide 15: Protocol Independent Multicast (PIM)
To develop a scalable protocol independent of any particular unicast protocol
  ANY unicast protocol to provide routing table
A router can switch between DM and SM depending on the group

## Slide 16: PIM Dense Mode
Deployed in resource rich environments
RPM Algorithm
  Similar to DVMRP
Algorithm
  A datagram is forwarded if the arriving interface is the shortest path back to the source
  Datagram forwarded on all outgoing interfaces initially
  Create forwarding cache entry
  Prune and graft messages used to prune the tree

## Slide 17
Leaf Network Detection
  Absence of PIM Hello messages
  No host membership reports
Pruning on a Multi-access LAN
  A prune is sent upstream when the outgoing interface list is empty
  Upstream router schedules the interface for deletion (Delay 3 sec)
  Any other routers on the LAN that depend on the upstream router send a PIM-Join
    Deletion request of interface cancelled
    Randomly delay Join message to reduce traffic
  Prunes are flushed periodically

## Slide 18
Graft and Graft ACKs
Designated Router in Multi-access LANs
  Highest IP address router as seen in “Hello”
Assert Messages
  When duplicate packets arrive on a multi-access LAN
  Send Assert with metric for that source
  Choose router with lower metric
  Equal metrics, higher IP address prevails
  Modify upstream and downstream neighbors

## Slide 19: Sparse - Mode
PIM-SM, CBT
Assumptions
  group members are sparsely distributed throughout the network
  BW not widely available
Receiver initiated construction of the spanning tree
    Limit multicast traffic and hence improve scalability
Define a Rendezvous Point (RP) and build the multicast tree around it

## Slide 20
Algorithm
  Sender sends data to the RP
  Receivers JOIN the RP tree
Difference from DM
  Receiver initiated vs Data Driven
  SM routers maintain state info ( Primary RP)
Advantages
  Conserve network resources
  Decreased amount of info in routers
Disadvantages
  Concentration of traffic around RP
  Sub-optimal trees increase Latency

## Slide 21: PIM Sparse Mode
Independent of particular unicast routing protocol
Algorithm
  Senders send data to the RP
  Receivers JOIN the tree
  Unwanted branches pruned
  Receivers can switch trees
R
R
R
R
R
R
R
S1
S2
Rendezvous
Point
Rendezvous
Point

## Slide 22
Designated Router
  Multiple routers on a LAN : Highest IP address
  Responsibilities
    IGMP Queries
    JOIN/Prune messages towards RP
    Maintain status of active RP
Route Entry
  Source address, Group Address
  Incoming interface (towards RP)
  Outgoing interfaces (towards receivers)
  WC-bit: Any source would match (*,G)
  RPT-bit: Join sent up the shared RP tree

## Slide 23
Receivers : when a new host report received
  Look up primary RP for that group
  Unicast JOIN message to the RP
    Payload: Address G, Join = RP, WC_bit, RPT_bit, PRUNE = NULL
  Create forwarding route entry for (*,G) pair
    Delete cache entry when no more members
  Intermediate routers transmit JOIN to RP
    Create forwarding route
    entry for (*,G)
Source (S)
Host
(receiver)
Designated
Router
Join
Join
Rendezvous Point
(RP)
for group G

## Slide 24
Hosts sending to Group
  Its DR looks up the active RP for that group
  Unicast data, encapsulated in a PIM-SM-Register to the RP
  Active RP sends a PIM-Join to the source DR
  Intermediate routers maintain state info (*,G)
  When source gets a Join, it sends further packets without encapsulation
  RP resends all data on the shared tree
Source (S)
Host
(receiver)
Host
(receiver)
RP
DR
PIM Router
Rendezvous Point
PIM-Register
PIM-Join
Resend to Group members

## Slide 25
  If data rate warrants an SPT, an (S,G) state created
    RP sends periodic Join/Prune to the source
    Intermediate routers maintain (S,G) state info
  Sources stop encapsulating data when they receive Register-Stop messages
    RP has no downstream members for that group or source
    RP already receives native data from (S,G) tree
Switching from RP-Shared tree to SPT
  Depending on the data rate of a particular source, a switch over may be initiated
    Only by RP or routers with members
  Activate (S,G) route entry

## Slide 26
  JOIN/PRUNE message from the rx towards the source
    Payload: Address G, Join = S, Prune = NULL
  Prune towards the RP for that (S,G)
Steady state of distribution tree
  Each router periodically sends JOIN/PRUNE for each active route entry
    To the neighbor indicated in the route entry
    Helps capture changes in topology/state/membership
Source (S)
Host
(receiver)
DR
RP
RP Tree
SP Tree

## Slide 27
RP Information
  Bootstrap messages are used to distribute RP information within the domain
  Domains’ Bootstrap Router (BSR) elected from set of candidates
  A set of RP candidates periodically advertise to the BSR the groups associated with them
  C-RP-Advertisements: Address of C-RP, Group address and mask
  C-RP-Advs distributed in BS messages
  The Advs are used by DRs
    use a Hash function to map a group address to one C-RP whose ad includes the group